FreeBSD Installation
FreeBSD Installation
AFNOG X
Cairo, Egypt
May 2009
Hervey Allen

---
Boot Off CD
READ THE INSTRUCTIONS
These slides contain explicit instructions to allow you to successfully install FreeBSD and Gnome on your machines.
If you do not read the instructions on these slides and/or do not pay attention to what is chosen in the screens during installation you are very likely to install incorrectly.
So:
READ THE INSTRUCTIONS
You instructors thank you :-)

---
Boot Off DVD
Insert the FreeBSD 7.2 DVD into your CD-ROM drive and (re)boot the machine. You may need to power cycle.

---
Sysinstall
Installation
Please follow the steps exactly as shown
FreeBSD Installer Keyboard Usage
- Move through it by using your up and down arrow keys, use the space or enter key to choose highlighted options.
- If there are “buttons” at the bottom of the screen, you can navigate to them by using the tab key then using the enter key.

---
Select Your Country

---
Select Keyboard

---
Select to Install FreeBSD
Use the tab key to select “Select” then enter to continue.

---
Confirm Geometry of Disk
We select “Yes” as our machines are “modern”

---
How Much of the Disk to Use
We will use our Entire Disk. Press “A” to do this.

---
Using the Entire Disk for FreeBSD
We chose the entire disk. Now press “Q” to leave this screen and continue with installation.

---
Now “Slice Up” your Disk (Partition)
The entire Disk is our FreeBSD partition. We now slice up our partition. Note that “ad0” is chosen by default.

---
Now “Slice Up” your Disk (Partition)
Choose “Auto Defaults” by pressing “A”, then exit the screen by pressing “Q”.
We will let the installer partition our slice for us. But, you can specify this
 any way you want. This is a very important step in the installation.

---
Options to Boot Your Machine
 If you have more than one Operating System on your machine, then you may want to choose “BootMgr”. In our case our machines will only have FreeBSD, so select “Standard”, tab to “OK” and press enter.

---
Install Everything
CAREFUL! You must do these steps exactly as follows:
Select “All”
Press the SPACE bar (Do not press enter!)

---
Install Ports – BIG Software Collection
Select “Yes” and press enter.

---
Choosing Distribution Part 2
Now we are returned to our Distribution selection menu. Notice that
 everything is chosen.
Now use the tab key to select “OK” and press enter.

---
Your Method of Installation
We have a single DVD for FreeBSD 7.2. Select “CD/DVD”, tab to “OK” and press enter to continue.

---
Post Install Configuration
We are now presented with a series of questions about items to configure after installation. Make the selections as shown.
Be sure “Yes” is chosen and press enter to continue

---
Choose a Network Interface
There are multiple network interfaces available to us. The one we are going to use will be highlighted by default. Select “OK” and press enter to continue.

---
IPv6
Select “No” and press enter. We may configure IPv6 later in the week.

---
Use DHCP for Network?
Select “No” and press enter. We will manually configure our network information as our machines are servers.

---
Configure Network
Use tab to move between fields. Once done, tab to “OK” and press enter. Note: change “pcN” to the actual name of your PC (pc1-pc16).

---
More Configuration
<= Choose “Yes”
<== Choose “Yes” here.

---
More Configuration continued
Note we choose “Yes” here.

---
Configuring Time and Time Zone
First select “Africa” to determine what Time Zone we are located in. Tab to “OK” and press enter.

---
Configuring Time Zone
Scroll to “Egypt”, tab to “OK” and press enter.

---
Configuring Time Zone cont.
Select “Yes” and press enter.

---
More Configuration
We will return to the package collection a bit later. For now be sure “No” is selected and press enter to continue.

---
User Configuration
We will create an initial user a bit later. Choose “No” for now.
Your class instructor will give you the password.

---
User Configuration Cont.
Verify the password. Then you will see...
Select “No” and press enter to continue.

---
Finishing Installation
We are back at our original screen. As we are done, select “Exit Install” and press enter.

---
Finishing Installation
Select “Yes” and press enter. Be sure to remove your FreeBSD 7.2 DVD-ROM from your machine.
After rebooting you can log in as “root” with the password you were given in class.
Our next set of instructions will lead you through the installation of the Gnome desktop manager.

---
This page intentionally left blank.

---
Installing Gnome
After you have logged in on your machine as the “root” user you will be presented with a “#” prompt. At this prompt type the command:
# sysinstall
You will be presented with the same menu that you saw when starting your FreeBSD installation. This time, however, we are going to do some “post-install configuration of FreeBSD”.
 Continue ==>

---
Installing Gnome Continued
Select “Configure”, tab to “Select” and press enter.

---
Installing Gnome: Packages
Next select “Packages”, tab to “OK” and press enter.

---
Installing Gnome: Install Media
Select “CD/DVD”, tab to “OK” and press enter.

---
Installing Gnome: Package Selection
Select “gnome”, tab to “OK” and press enter.

---
Installing Gnome: Package Selection
There are a lot of gnome packages. We are looking for the meta package, or “gnome2-2.26.0”. Move your cursor to this line and then press the space bar to select this.

---
Installing Gnome: Package Selected
Notice what happens. All Dependent packages for gnome2-2.26.0 are automatically chosen. Now use tab to select “OK” and press enter.

---
Installing Gnome: Package Install
You are returned to the Package Selection screen, but note that you now have an “Install” option. Be sure to select “Install” and press enter.

---
Installing Gnome: Verify Choice
Be sure “OK” is chosen and then press enter to install Gnome.
You will now see a lot of packages being installed. Installation will take a few minutes. Once installation has completed you will see a final sysinstall screen.
Continued ==>

---
Installing Gnome: Config Menu
You are returned to the sysinstall Configuration Menu. Be sure “X Exit” is chosen, tab to “OK” and press enter.

---
Installing Gnome: Exit Menu
We are returned to the sysinstall Main Menu. Use tab to select “X Exit Install” and press enter. You are almost done.

---
Installing Gnome: Cleanup
You should now have the “#” prompt on your screen.
In FreeBSD version 7.2 (May 2009) Gnome 2.26-0 and the Graphical Display Manager version 2.26.0_1 have some small configuration issues. We must clean up after these to complete our installation.
First we will add an entry for the “proc” file system in our /etc/fstab file. This is a file system that exists in Linux. We define this for our environment as Gnome makes use of proc if available. We must edit the file /etc/fstab:
# vi /etc/fstab
Go to the bottom of the file, press the “o” key and add this line:
proc	/proc	procfs	rw	0	0
Now press Esc, then type “:wq” to exit and save the file.

---
Installing Gnome: Cleanup Cont.
You should now have the “#” prompt, once again, on your screen.
Now we must edit the file /etc/rc.conf and add one other line. This will cause Gnome to start whenever we boot our machine.
# vi /etc/rc.conf
Now go to the bottom of the file and press the “o” key to add a blank line. Add the following entry:
gnome_enable=”YES”
Now press Esc, then type “:wq” to exit and save the file. You should be back at the “#” prompt.

---
Installing Gnome: Finish
Now we will create a user other than root that we will use when logging in with Gnome. We will call this user inst and this will be our administrative user that we use throughout the workshop.
# pw useradd inst -m -s /usr/local/bin/bash -G wheel
This user has a home directory, uses bash as its default shell and belongs to the wheel group.
While not necessary, we will now reboot our machine so that you can see the new default behaviour. At the prompt type:
# shutdown -r now
Upon rebooting you should be presented with the Gnome graphical login prompt. Don't log in as the root user, rather use the inst user to log in at this point. Enjoy!