IP network tools & troubleshooting
AFNOG X
Cairo, Egypt
May 2009

---
Network configuration
Reminder, configure your network in /etc/rc.conf ( x = your IP, from .100 to ...)
ifconfig_em0=”196.200.218.x/24”
defaultrouter=”196.200.218.254”
ipv6_enable="YES" ipv6_ifconfig_em0="2001:4348:0:218:196:200:218:x"
ipv6_defaultrouter=” 2001:4348:0:218:196:200:218:254"

---
Network configuration
You can do this from the command line:
ifconfig em0 196.200.218.x/24
route add default 196.200.218.254
ifconfig em0 inet6 2001:4348:0:218:196:200:218:x
route add -inet6 default
2001:4348:0:218:196:200:218:254

---
The IP end-to-end principle
- IP is an end-to-end protocol
- The network doesn't keep track of connections
- The host takes a decision on where to send each packet
- The network equipment takes a decision on where to forward packets every time
- The path is not necessarily symmetric
- Cost constraints, reconfiguration of the network, network failures can make the IP packets

---
IP path
End-to-End
PING
PING
PING
PING
PONG
PONG
PONG
PONG
PING
PONG

---
IP path
End-to-End
PING
PING
PING
PING
PONG
PONG
PONG
PONG
PING
PONG
PONG

---
IP path
End-to-End
TIMEOUT
PING
PING
PING
PING
PONG
PONG
PING

---
Network tools
- What network tools can we use to troubleshoot ?
- ping – requests echo reply from a computer
- traceroute – show path taken by IP packets
  through a	network
- tcpdump – show network traffic
- netstat – show routing entries and
  listening/active sockets
- arp – show/modify the IP <-> MAC address table
- ndp – show debug/ndp (Neighb. Disc. Protocol)‏
- route – show/modify the routing table
- mtr – combines ping & traceroute

---
ping
- usage:
  ping hostname_or_IP_address
  ping6 hostname_or_IPv6_address
- ping sends an ICMP/ICMP6 echo request (type 8), and the responsing host sends an ICMP/ICMP6 echo reply (type 0)
- ICMP and ICMP6 sit on top of IP, side by side with TCP and UDP

---
ping – sample output
# ping 196.200.218.254
PING 196.200.218.254 (196.200.218.254): 56 data bytes
64 bytes from 196.200.218.254: icmp_seq=0 ttl=255 time=0.424 ms
64 bytes from 196.200.218.254: icmp_seq=1 ttl=255 time=0.429 ms
64 bytes from 196.200.218.254: icmp_seq=2 ttl=255 time=0.468 ms
...
# ping6 2001:4348:0:223:196:200:223:254
PING6(56=40+8+8 bytes) 2001:4348:0:218:196:200:218:1 --> 2001:4348:0:223:196:200:223:254
16 bytes from 2001:4348:0:223:196:200:223:254, icmp_seq=0 hlim=64 time=0.426 ms
16 bytes from 2001:4348:0:223:196:200:223:254, icmp_seq=1 hlim=64 time=0.451 ms
16 bytes from 2001:4348:0:223:196:200:223:254, icmp_seq=2 hlim=64 time=0.446 ms

---
Traceroute
- discover path taken by packets on the way to another host
- usage:
  $ traceroute [-n] hostname_or_IP
  ( -n == no DNS lookup )
# traceroute afnog.org
traceroute to afnog.org (196.216.2.34), 64 hops max, 40 byte packets
 1 196.200.218.254 (196.200.218.254) 0.435 ms 0.323 ms 0.311 ms
 2 ll81-2-205-33-192-81.ll81-2.iam.net.ma (81.192.33.205) 1.628 ms 1.330 ms 1.367 ms
 3 172.20.2.31 (172.20.2.31) 1.485 ms 1.517 ms 1.423 ms
 4 ppp-20-3-217-212.dialup.iam.net.ma (212.217.3.20) 1.360 ms 1.376 ms 1.443 ms
 5 pal2-almaghrib-2.pal.seabone.net (195.22.197.41) 58.213 ms 58.178 ms 58.205 ms
 6 POS4-3.BR1.LND9.ALTER.NET.25 (146.188.70.25) 70.771 ms 68.942 ms 70.539 ms

---
Traceroute - IPv6
usage:
$ traceroute6 [-n] hostname_or_IPv6
( -n == no DNS lookup )
# traceroute6 -n x1.x0.dk
traceroute6 to x1.x0.dk (2001:41d0:1:2cc8::1) from
2001:4348:0:218:196:200:218:1, 64 hops max, 12 byte packets
 1 2001:4348:0:218:196:200:218:254 0.449 ms 0.363 ms 0.338 ms
 2 2001:418:1:101::1 232.759 ms * 232.122 ms
 3 * 2001:418:0:5000::25 252.862 ms 232.198 ms
 4 2001:450:2008:1020::2 235.555 ms 232.634 ms 232.478 ms

---
Traceroute – how does it work ?
uses the TTL property of IP packets
  - send the first packet with a TTL of 1, to the destination host.
  - the gateway sees the TTL of 1, decrements it to 0, and returns a “TTL expired” message to the sending host
  - send the second packet, still for the destination host, but this time with a TTL of 2
  - the first gateway lets the packet go through, decrements the TTL from 2 to 1, and passes it on to the next hop
  - the second gateway decrements the TTL from 1 to 0, and returns a TTL expired message to the sending host
  - etc...

---
netstat
- Allows you to view the status of your network
- The routing table - usage:
  $ netstat [-n] -r # v4,v6
  $ netstat [-n] -r -f inet	# ipv4
  $ netstat [-n] -r -f inet6	# ipv6
$ netstat -n -r -f inet
Routing tables
Internet:
Destination Gateway Flags Refs Use Netif Expire
default 196.200.218.254 UGS 0 1024 em0
127.0.0.1 127.0.0.1 UH 0 0 lo0
196.200.218.0/24 link#1 UC 0 0 em0
196.200.218.105 00:1e:0b:b5:a3:f9 UHLW 1 1 em0 1198
196.200.218.254 00:1c:58:22:1c:e0 UHLW 2 22 em0 1162

---
netstat
The open connections and listening sockets:
$ netstat [-n] -a
$ netstat -a -n
Active Internet connections (including servers)‏
Proto Recv-Q Send-Q Local Address Foreign Address (state)‏
tcp4 0 0 196.200.218.1.22 196.200.216.49.63843 ESTABLISHED
tcp4 0 0 *.22 *.* LISTEN
tcp6 0 0 *.22 *.* LISTEN
udp4 0 0 *.514 *.*
udp6 0 0 *.514 *.*
Active UNIX domain sockets
Address Type Recv-Q Send-Q Inode Conn Refs Nextref Addr
c55155e8 stream 0 0 c556c770 0 0 0 /tmp/ssh-1To0610lI7/agent.983
...

---
ARP
- Used to show IPv4 <-> MAC address lookup tables
- Usually ethernet
- Usage:
  $ arp -a
$ arp -a
? (196.200.218.105) at 00:1e:0b:b5:a3:f9 on em0 [ethernet]
? (196.200.218.254) at 00:1c:58:22:1c:e0 on em0 [ethernet]

---
ARP on v6 ?
- No ARP on v6...
- Use 'ndp'
test# ndp -a
Neighbor Linklayer Address Netif Expire S Flags
2001:4348:0:218:196:200:218:1 0:1e:b:b2:f7:e0 em0 20h35m18s S
2001:4348:0:218:196:200:218:200 0:1e:b:b5:a3:c9 em0 permanent R
2001:4348:0:218:196:200:218:254 0:1c:58:22:1c:e0 em0 17h15m2s S R
fe80::21c:58ff:fe22:1ce0%em0 0:1c:58:22:1c:e0 em0 17h14m43s S R
fe80::21e:bff:feb5:a3c9%em0 0:1e:b:b5:a3:c9 em0 permanent R
fe80::1%lo0 (incomplete) lo0 permanent R

---
The route command
The route command it used to modify or query the routing table. Examples for IPv4:
route [-n] get default
route add 196.216.2.34 196.200.218.254
route add default 196.200.218.253
route change default 196.200.218.254
# route get default
   route to: default
destination: default
       mask: default
    gateway: 196.200.218.254
  interface: em0
      flags: <UP,GATEWAY,DONE,STATIC>
...

---
The route command
Examples for IPv6
route [-n] get -inet6 default
route add 2001:4348:0:223:196:200:223:1
2001:4348:0:218:196:200:218:254
route add -inet6 default
2001:4348:0:218:196:200:218:254
route change -inet6 default
2001:4348:0:218:196:200:218:254
 route -n get -inet6 default
   route to: ::
destination: ::
       mask: default
    gateway: 2001:4348:0:218:196:200:218:254
  interface: em0
      flags: <UP,GATEWAY,DONE,STATIC>
...

---
tcpdump
- tcpdump used to view network traffic on the wire
- basic usage:
  # tcpdump [-e] [-n] -i if0 [expr.]
  ... where if0 is your interface (e.g.: em0)
- To set how much data you want to see, use the '-s' option, for example: -s1500
- Expr limits the traffic to certain types (default IPv4)
  # tcpdump -n -i em0 icmp
  # tcpdump -n -i em0 -s1500 tcp and not port 22
  # tcpdump -n -i em0 icmp6

---
tcpdump
Example:
# tcpdump -n -i em0
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on em0, link-type EN10MB (Ethernet), capture size 96 bytes
23:04:55.854924 IP 196.200.218.1.22 > 196.200.216.49.63843: P 1471203813:1471204005(192) ack 2536290644 win 8326 <nop,nop,timestamp 767233219 810276026>
23:04:55.859489 IP 196.200.216.49.63843 > 196.200.218.1.22: . ack 0 win 33280 <nop,nop,timestamp 810276026 767233218>
23:04:55.864256 IP 196.200.216.49.63843 > 196.200.218.1.22: . ack 192 win 33208 <nop,nop,timestamp 810276026 767233219>
23:04:56.204079 IP 196.200.216.49 > 196.200.218.1: ICMP echo request, id 55424, seq 2, length 64
23:04:56.204084 IP 196.200.218.1 > 196.200.216.49: ICMP echo reply, id 55424, seq 2, length 64

---
Tcpdump - IPv6
Example (with -e to see ethernet addresses)‏
# tcpdump -e -ni em0 ip6
19:44:43.434075 00:1e:0b:b2:f7:e0 > 33:33:ff:18:02:00, ethertype IPv6 (0x86dd), length 86: 2001:4348:0:218:196:200:218:1 > ff02::1:ff18:200: ICMP6, neighbor solicitation, who has 2001:4348:0:218:196:200:218:200, length 32
19:44:43.434104 00:1e:0b:b5:a3:c9 > 00:1e:0b:b2:f7:e0, ethertype IPv6 (0x86dd), length 86: 2001:4348:0:218:196:200:218:200 > 2001:4348:0:218:196:200:218:1: ICMP6, neighbor advertisement, tgt is 2001:4348:0:218:196:200:218:200, length 32
19:44:43.434496 00:1e:0b:b2:f7:e0 > 00:1e:0b:b5:a3:c9, ethertype IPv6 (0x86dd), length 70: 2001:4348:0:218:196:200:218:1 > 2001:4348:0:218:196:200:218:200: ICMP6, echo request, seq 0, length 16
19:44:43.434505 00:1e:0b:b5:a3:c9 > 00:1e:0b:b2:f7:e0, ethertype IPv6 (0x86dd), length 70: 2001:4348:0:218:196:200:218:200 > 2001:4348:0:218:196:200:218:1: ICMP6, echo reply, seq 0, length 16

---
mtr
- Can be obtained with pkg_add -r mtr
- Combines traceroute & ping – works with v4 & v6
# mtr x1.x0.dk
Keys: Help Display mode Restart statistics Order of fields quit
        Packets Pings
 Host Loss% Snt Last Avg Best Wrst StDev
 1. 2001:4348::216:196:200:217 0.0% 6 2.5 2.7 2.5 2.9 0.2
 2. 2001:418:1:101::1 0.0% 6 235.0 235.6 234.0 238.7 1.8
 3. fa-4-6.r00.sttlwa01.us.bb 16.7% 6 239.5 239.1 234.8 249.7 6.2
 4. 2001:450:2008:1020::2 0.0% 6 235.1 234.9 234.1 235.9 0.6
 5. ???
 6. ???
 7. ???
 8. ???
 9. ???
10. 2001:41d0:1:2cc8::1 0.0% 5 406.8 405.9 402.0 409.0 2.6

---
Questions ?