IP and Networking Basics
Scalable Infrastructure Workshop
AfNOG 2009

---
The (capital “I”) Internet
- The world-wide network of TCP/IP networks
- Different people or organisations own different parts
- Different parts use different technologies
- Interconnections between the parts
- Interconnections require agreements
  - sale/purchase of service
  - contracts
  - “peering” agreements
No central control or management

---
A small internetwork or (small “i”) “internet”

---
The principle of “Internetworking”
- We have lots of little networks
- Many different owners/operators
- Many different types
  - Ethernet, dedicated leased lines, dialup, optical, broadband, wireless, ...
- Each type has its own idea of low level addressing and protocols
- We want to connect them all together and provide a unified view of the whole lot (treat the collection of networks as a single large internetwork)‏

---
OSI Stack & TCP/IP Architecture

---
The unifying effect of the network layer
- Define a protocol that works in the same way with any underlying network
- Call it the network layer (e.g. IP)‏
- IP routers operate at the network layer
- IP over anything
- Anything over IP

---
The TCP/IP Hourglass Model
Application layer
Transport layer
Network layer
Physical and Data link layer
PPP
ATM
Optics
ADSL
Satellite
3G
Ethernet
IP
UDP
TCP
HTTP
FTP
Telnet
DNS
SMTP
Audio
Video
RTP

---
The OSI Model
Upper Layers
Application oriented
(Almost) independent of layers below
Lower Layers
Transmission of data
Independent of upper layers
1
3
2
4
5
6
7
Application
Presentation
Session
Transport
Network
 Data Link
Physical

---
OSI Model and the Internet
- Internet protocols are not directly based on the OSI model
- However, we do often use the OSI numbering system:
  - Layer 7: Application
  - Layer 4: Transport (e.g. TCP)
  - Layer 3: Network (IP)
  - Layer 2: Data link
  - Layer 1: Physical

---
Corresponding layers in the OSI and TCP/IP models
Mail, Web, etc.
TCP/UDP – end to end reliability
IP - Forwarding (best-effort)‏
Framing, delivery
Raw signal
OSI
TCP/IP
1
3
2
4
5
6
7
Application
Presentation
Session
Transport
Network
 Data Link
Physical
Application
Transport
Network
Data Link &
Physical
[Speaker Notes: This diagram shows the mapping between the OSI and the TCP/IP model. The OSI models further divides the application layer in the TCP/IP into separate layers, each with its own function]

---
Layer Interaction:
TCP/IP Model
End to end
Hop by hop
Router
Host
Host
Router
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical

---
End-to-end layers
- Upper layers are “end-to-end”
- Applications at the two ends behave as if they can talk directly to each other
- They do not concern themselves with the details of what happens in between

---
Hop-by-hop layers
- At the lower layers, devices share access to the same physical medium
- Devices communicate directly with each other
- The network layer (IP) has some knowledge of how many small networks are interconnected to make a large internet
- Information moves one hop at a time, getting closer to the destination at each hop

---
Layer Interaction:
The Application Layer
Applications behave as if they can talk to each other, but in reality the application at each side talks to the TCP or UDP service below it.
The application layer doesn't care about what happens at the lower layers, provided the transport layer carries the application's data safely from end to end.
Router
Host
Host
Router
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical

---
Layer Interaction:
The Transport Layer
The transport layer instances at the two ends act as if they are talking to each other, but in reality they are each talking to the IP layer below it. The transport layer doesn't care about what the application layer is doing above it.
The transport layer doesn't care what happens in the IP layer or below, as long as the IP layer can move datagrams from one side to the other.
Router
Host
Host
Router
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical

---
Layer Interaction:
The Network Layer (IP)
The IP layer has to know a lot about the topology of the network (which host is connected to which router, which routers are connected to each other), but it doesn't care about what happens at the upper layers.
The IP layer works forwards messages hop by hop from one side to the other side.
Router
Host
Host
Router
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical

---
Layer Interaction:
Link and Physical Layers
The link layer doesn't care what happens above it, but it is very closely tied to the physical layer below it.
All links are independent of each other, and have no way of communicating with each other.
Router
Host
Host
Router
Application
TCP or UDP
IP
Link
Physical
IP
Link
Link
IP
Link
Link
Application
TCP or UDP
IP
Link
Physical
Physical

---
Encapsulation & Decapsulation
Lower layers add headers (and sometimes trailers) to data from higher layers
Data
Application
Header
Transport Layer Data
Transport
Header
Network Layer Data
Network
Header
Header
Data
Network
Trailer
Header
Link Layer Data
Data Link
Header
Header
Header
Data
Trailer
Data Link

---
Frame, Datagram, Segment, Packet
Different names for packets at different layers
  - Ethernet (link layer) frame
  - IP (network layer) datagram
  - TCP (transport layer) segment
Terminology is not strictly followed
  - we often just use the term “packet” at any layer

---
Layer 2 - Ethernet frame
6 bytes
6 bytes
2 bytes
2 bytes
46 to 1500 bytes
4 bytes
- Destination and source are 48-bit MAC addresses
- Type 0x0800 means that the “data” portion of the Ethernet frame contains an IPv4 datagram. Type 0x0806 for ARP. Type 0x86DD for IPv6.
- “Data” part of layer 2 frame contains a layer 3 datagram.
Preamble
Dest
Source
Length
Data
CRC
Type

---
Layer 3 - IPv4 datagram
Version = 4
If no options, IHL = 5
Source and Destination are 32-bit IPv4 addresses
Protocol = 6 means data portion contains a TCP segment. Protocol = 17 means UDP.
IHL
Type of Service
Total Length
Version
Fragment Offset
Identification
Flags
Time to Live
Protocol
Header Checksum
Source Address (32-bit IPv4 address)‏
Destination Address (32-bit IPv4 address)‏
Data (contains layer 4 segment)‏
Padding
Options

---
Layer 4 - TCP segment
- Source and Destination are 16-bit TCP port numbers (IP addresses are implied by the IP header)‏
- If no options, Data Offset = 5 (which means 20 octets)‏
Source Port
Destination Port
Sequence Number
Acknowledgement Number
Data Offset
Window
Reserved
ACK
URG
EOL
RST
SYN
FIN
Checksum
Urgent Pointer
Data (contains application data)‏
Padding
Options

---
IP Addressing

---
Purpose of an IPv4 address
Unique Identification of:
  - Source
    - So the recipient knows where the message is from
    - Sometimes used for security or policy-based filtering of data
  - Destination
    - So the networks know where to send the data
Network Independent Format
  - IP over anything

---
Purpose of an IPv4 Address
- Identifies a machine’s connection to a network
- Physically moving a machine from one network to another requires changing the IP address
- Unique; assigned in a hierarchical fashion
  - IANA to RIRs (AfriNIC, ARIN, RIPE, APNIC, LACNIC)‏
  - RIR to ISPs and large organisations
  - ISP or company IT department to end users
- IPv4 uses unique 32-bit addresses
- IPv6 used similar concepts but 128-bit addresses

---
Basic Structure of an IPv4 Address
- 32 bit number (4 octet number):
  (e.g. 133.27.162.125)‏
- Decimal Representation:
Binary Representation:
Hexadecimal Representation:
133
27
162
125
10000101
00011011
10100010
01111101
85
1B
A2
7D

---
Address Exercise
SWITCH
E
PC
Router
D
PC
Router
C
PC
Router
B
PC
Router
A
PC
Router
F
PC
Router
G
PC
Router
H
PC
Router
I
PC
Router
J
PC
Router

---
Address Exercise
- Construct an IP address for your router’s connection to the backbone network.
- 196.200.220.x
- x = 1 for row A, 2 for row B, etc.
- Write it in decimal form as well as binary form.

---
Addressing in Internetworks
The problem we have
  - More than one physical network
  - Different Locations
  - Larger number of hosts
  - Need a way of numbering them all
- We use a structured numbering system
  - Hosts that are connected to the same physical network have “similar” IP addresses
  - Often more then one level of structure; e.g. physical networks in the same organisation use “similar” IP addresses

---
Network part and
Host part
- Remember IPv4 address is 32 bits
- Divide it into a “network part” and “host part”
  - “network part” of the address identifies which network in the internetwork (e.g. the Internet)‏
  - “host part” identifies host on that network
  - Hosts or routers connected to the same link-layer network will have IP addresses with the same network part, but different host part.
  - Host part contains enough bits to address all hosts on the subnet; e.g. 8 bits allows 256 addresses

---
Dividing an address
Hierarchical Division in IP Address:
  - Network Part (or Prefix) – high order bits (left)‏
    - describes which physical network
  - Host Part – low order bits (right)‏
    - describes which host on that network
  - Boundary can be anywhere
    - choose the boundary according to number of hosts
    - very often NOT a multiple of 8 bits
Host Part
Network Part

---
Network Masks
- “Network Masks” help define which bits are used to describe the Network Part and which for the Host Part
- Different Representations:
  - decimal dot notation: 255.255.224.0
  - binary: 11111111 11111111 11100000 00000000
  - hexadecimal: 0xFFFFE000
  - number of network bits: /19
    - count the 1's in the binary representation
Above examples all mean the same: 19 bits for the Network Part and 13 bits for the Host Part

---
Example Prefixes
137.158.128.0/17	(netmask 255.255.128.0)‏
198.134.0.0/16	(netmask 255.255.0.0)‏
205.37.193.128/26 (netmask 255.255.255.192)
1111 1111
1111 1111
1 000 0000
0000 0000
1111 1111
1111 1111
0000 0000
0000 0000
1111 1111
1111 1111
1111 1111
11 00 0000
1000 1001
1001 1110
1 000 0000
0000 0000
1100 0110
1000 0110
0000 0000
0000 0000
1100 1101
0010 0101
1100 0001
10 00 0000

---
Special Addresses
All 0’s in host part: Represents Network
  - e.g. 193.0.0.0/24
  - e.g. 138.37.64.0/18
  - e.g. 196.200.223.96/28
All 1’s in host part:	Broadcast
  - e.g. 193.0.0.255 (prefix 193.0.0.0/24)‏
  - e.g. 138.37.127.255 (prefix 138.37.64.0/18)‏
  - e.g. 196.200.223.111 (prefix 196.200.223.96/28)‏
- 127.0.0.0/8: Loopback address (127.0.0.1)‏
- 0.0.0.0: Various special purposes

---
Exercise
- Verify that the previous examples are all broadcast addresses:
  - 193.0.0.255 (prefix 193.0.0.0/24)‏
  - 138.37.127.255 (prefix 138.37.64.0/18)‏
  - 196.200.223.111 (prefix 196.200.223.96/28)‏
Do this by finding the boundary between network part and host part, and checking that the host part (if written in binary) contains all 1's.

---
Maximum number of hosts per network
- The number of bits in the host part determines the maximum number of hosts
- The all-zeros and all-ones addresses are reserved, can't be used for actual hosts
- E.g. a subnet mask of 255.255.255.0 or /24 means 24 network bits, 8 host bits (24+8=32)‏
  - 28 minus 2 = 254 possible hosts
Similarly a subnet mask of 255.255.255.224 or /27 means 27 network bits, 5 host bits (27+5=32)‏
  - 25 minus 2 = 30 possible hosts

---
More Address Exercises
Assuming there are 15 routers on the classroom backbone network:
  - what is the minimum number of host bits needed to address each router with a unique IP address?
  - with that many host bits, how many network bits?
  - what is the corresponding prefix length in “slash” notation?
  - what is the corresponding netmask (in decimal)?
  - with that netmask, what is the maximum number of hosts?

---
More levels of address hierarchy
Extend the concept of “network part” and “host part”:
  - arbitrary number of levels of hierarchy
  - blocks don’t all need to be the same size
  - but each block size must be a power of 2
- Very large blocks allocated to RIRs (e.g. /8)
  - Divided into smaller blocks for ISPs (e.g. /17)
    - Divided into smaller blocks for businesses (e.g. /22)
      - Divided into smaller blocks for local networks (e.g. /26)
        - Each host gets a host address

---
Ancient History: Classful Addressing
- Nowadays, we always explicitly say where the boundary between network part and host part is
  - using slash notation or netmask notation
- Old systems used restrictive rules (obsolete)‏
  - Called “Class A”, “Class B”, “Class C” networks
  - Boundary between network part and host part was implied by the class
Nowadays (since 1994), no restriction
  - Called “classless” addressing, “classless” routing

---
Ancient History: Sizes of classful networks
Different classes were used to represent different sizes of network (small, medium, large)‏
Class A networks (large):
  - 8 bits network part, 24 bits host part
Class B networks (medium):
  - 16 bits network part, 16 bits host part
Class C networks (small):
  - 24 bits network part, 8 bits host part

---
Ancient History: What class is my address?
Just look at the address to tell what class it is.
  - Class A: 0.0.0.0 to 127.255.255.255
    - binary 0nnnnnnnhhhhhhhhhhhhhhhhhhhhhhhh
  - Class B: 128.0.0.0 to 191.255.255.255
    - binary 10nnnnnnnnnnnnnnhhhhhhhhhhhhhhhh
  - Class C: 192.0.0.0 to 223.255.255.255
    - binary 110nnnnnnnnnnnnnnnnnnnnnhhhhhhhh
  - Class D: (multicast) 224.0.0.0 to 239.255.255.255
    - binary 1110xxxxxxxxxxxxxxxxxxxxxxxxxxxx
  - Class E: (reserved) 240.0.0.0 to 255.255.255.255

---
Ancient History: Implied netmasks
A classful network had a “natural” or “implied” prefix length or netmask:
  - Class A: prefix length /8 (netmask 255.0.0.0)‏
  - Class B: prefix length /16 (netmask 255.255.0.0)‏
  - Class C: prefix length /24 (netmask 255.255.255.0)‏
Modern (classless) routing systems have explicit prefix lengths or netmasks
  - You can't just look at an IP address to tell what the prefix length or netmask should be. Protocols and configurations need explicit netmask or prefix length.

---
Classless Addressing
Class A, Class B, Class C terminology and restrictions are now of historical interest only
  - Obsolete in 1994
- Internet routing and address management today is classless
- CIDR = Classless Inter-Domain Routing
  - routing does not assume that class A, B, C implies prefix length /8, /16, /24
VLSM = Variable-Length Subnet Masks
  - routing does not assume that all subnets are the same size

---
Classless addressing example
An ISP gets a large block of addresses
  - e.g., a /16 prefix, or 65536 separate addresses
Allocate smaller blocks to customers
  - e.g., a /22 prefix (1024 addresses) to one customer, and a /28 prefix (16 addresses) to another customer (and some space left over for othe customers)
An organisation that gets a /22 prefix from their ISP divides it into smaller blocks
  - e.g. a /26 prefix (64 addresses) for one department, and a /27 prefix (32 addresses) for another department (and some space left over for other internal networks)

---
Classless addressing exercise
- Consider the address block 133.27.162.0/23
- Allocate 5 separate /29 blocks, one /27 block, and one /25 block
- What are the IP addresses of each block allocated above?
  - in prefix length notation
  - netmasks in decimal
  - IP address ranges
- What blocks are still available (not yet allocated)?
- How big is the largest available block?

---
IPv6

---
IP version 6
IPv6 designed as successor to IPv4
  - Expanded address space
    - Address length quadrupled to 16 bytes (128 bits)‏
  - Header Format Simplification
    - Fixed length, optional headers are daisy-chained
  - No checksum at the IP network layer
  - No hop-by-hop fragmentation
    - Path MTU discovery
  - 64 bits aligned fields in the header
  - Authentication and Privacy Capabilities
    - IPsec is mandated
  - No more broadcast

---
IPv4 and IPv6 Header Comparison
IPv6 Header
IPv4 Header
Field’s name kept from IPv4 to IPv6
Fields not kept in IPv6
Name and position changed in IPv6
New field in IPv6
Legend
Next Header
Hop Limit
Flow Label
Traffic Class
Destination Address
Source Address
Payload Length
Version
Fragment Offset
Flags
Total Length
Type of Service
IHL
Padding
Options
Destination Address
Source Address
Header Checksum
Protocol
Time to Live
Identification
Version

---
Larger Address Space
IPv4 = 32 bits
IPv6 = 128 bits
  - IPv4
    - 32 bits
    - = 4,294,967,296 possible addressable devices
  - IPv6
    - 128 bits: 4 times the size in bits
    - = 3.4 x 1038 possible addressable devices
    - = 340,282,366,920,938,463,463,374,607,431,768,211,456
    -  5 x 1028 addresses per person on the planet

---
IPv6 Address Representation
16 bit fields in case insensitive colon hexadecimal representation
  - 2031:0000:130F:0000:0000:09C0:876A:130B
Leading zeros in a field are optional:
  - 2031:0:130F:0:0:9C0:876A:130B
Successive fields of 0 represented as ::, but only once in an address:
  - 2031:0:130F::9C0:876A:130B	is ok
  - 2031::130F::9C0:876A:130B	is NOT ok (two “::”)‏
  - 0:0:0:0:0:0:0:1  ::1	(loopback address)‏
  - 0:0:0:0:0:0:0:0  ::	(unspecified address)‏

---
IPv6 Address Representation
In a URL, it is enclosed in brackets (RFC3986)‏
  - http://[2001:db8:4f3a::206:ae14]:8080/index.html
  - Cumbersome for users
  - Mostly for diagnostic purposes
  - Use fully qualified domain names (FQDN)‏ instead of this
Prefix Representation
  - Representation of prefix is same as for IPv4 CIDR
    - Address and then prefix length, with slash separator
  - IPv4 address:
    - 198.10.0.0/16
  - IPv6 address:
    - 2001:db8:12::/40

---
IPv6 Addressing
::/128
    0000…0000
Unspecified
::1/128
    0000…0001
Loopback
FF00::/8
    1111 1111 ...
Multicast Address
FC00::/7
    1111 1100 ...
    1111 1101 ...
Unique Local Unicast Address
FE80::/10
    1111 1110 10...
Link Local Unicast Address
2000::/3
    0010 ...
Global Unicast Address
Hex
Binary
Type
[Speaker Notes: The actual addressing scheme of IPv6]

---
IPv6 Global Unicast Addresses
Provider
Site
Host
48 bits
16 bits
64 bits
Global Routing Prefix
Subnet-id
Interface ID
001
IPv6 Global Unicast addresses are:
  - Addresses for generic use of IPv6
  - Hierarchical structure intended to simplify aggregation

---
IPv6 Address Allocation
/12
/48
/64
/32
2000
 0db8
Interface ID
Registry
ISP prefix
Site prefix
LAN prefix
The allocation process is:
  - The IANA is allocating out of 2000::/3 for initial IPv6 unicast use
  - Each registry gets a /12 prefix from the IANA
  - Registry allocates a /32 prefix (or larger) to an IPv6 ISP
  - Policy is that an ISP allocates a /48 prefix to each end customer

---
IPv6 Addressing Scope
64 bits reserved for the interface ID
  - Possibility of 264 hosts on one network LAN
  - Arrangement to accommodate MAC addresses within the IPv6 address
16 bits reserved for the end site
  - Possibility of 216 networks at each end-site
  - 65536 subnets equivalent to a /12 in IPv4 (assuming 16 hosts per IPv4 subnet)‏

---
IPv6 Addressing Scope
16 bits reserved for the service provider
  - Possibility of 216 end-sites per service provider
  - 65536 possible customers: equivalent to each service provider receiving a /8 in IPv4 (assuming a /24 address block per customer)‏
32 bits reserved for service providers
  - Possibility of 232 service providers
  - i.e. 4 billion discrete service provider networks
    - Although some service providers already are justifying more than a /32
  - Equivalent to the size of the entire IPv4 address space

---
Summary
- Vast address space
- Hexadecimal addressing
- Distinct addressing hierarchy between ISPs, end-sites, and LANs
  - ISPs have /32s
  - End-sites have /48s
  - LANs have /64s
Other IPv6 features discussed later

---
Large Network Issues
& Routers

---
The need for Packet Forwarding
- Many small networks can be interconnected to make a larger internetwork
- A device on one network cannot send a packet directly to a device on another network
- The packet has to be forwarded from one network to another, through intermediate nodes, until it reaches its destination
- The intermediate nodes are called “routers”

---
An IP Router
- A device with more than one link-layer interface
- Different IP addresses (from different subnets) on different interfaces
- Receives packets on one interface, and forwards them (usually out of another interface) to get them one hop closer to their destination
- Maintains forwarding tables

---
IP router - action for each packet
- Packet is received on one interface
- Checks whether the destination address is the router itself – if so, pass it to higher layers
- Decrement TTL (time to live), and discard packet if it reaches zero
- Look up the destination IP address in the forwarding table
- Destination could be on a directly attached link, or through another router

---
Forwarding is hop by hop
- Each router tries to get the packet one hop closer to the destination
- Each router makes an independent decision, based on its own forwarding table
- Different routers have different forwarding tables and make different decisions
  - If all is well, decisions will be consistent
Routers talk routing protocols to each other, to help update routing and forwarding tables

---
Hop by Hop Forwarding

---
Router Functions
Determine optimum routing paths through a network
  - Lowest delay
  - Highest reliability
Move packets through the network
  - Examines destination address in packet
  - Makes a decision on which port to forward the packet through
  - Decision is based on the Routing Table
- Interconnected Routers exchange routing tables in order to maintain a clear picture of the network
- In a large network, the routing table updates can consume a lot of bandwidth
  - a protocol for route updates is required

---
Forwarding table structure
- We don't list every IP number on the Internet - the table would be huge
- Instead, the forwarding table contains prefixes (network numbers)
  - "If the first /n bits matches this entry, send the datagram thataway"
- If more than one prefix matches, the longest prefix wins (more specific route)
- 0.0.0.0/0 is "default route" - matches anything, but only if no other prefix matches

---
ARP

---
Encapsulation Reminder
Lower layers add headers (and sometimes trailers) to data from higher layers
Data
Application
Header
Transport Layer Data
Transport
Header
Network Layer Data
Network
Header
Header
Data
Network
Trailer
Header
Link Layer Data
Data Link
Header
Header
Header
Data
Trailer
Data Link

---
Ethernet Essentials
- Ethernet is a broadcast medium
- Structure of Ethernet frame:
- Entire IP packet makes data part of Ethernet frame
- Delivery mechanism (CSMA/CD)‏
  - back off and try again when collision is detected
Preamble
Dest
Source
Length
Data
CRC
Type

---
Ethernet/IP Address Resolution
Internet Address
  - Unique worldwide (excepting private nets)‏
  - Independent of Physical Network technology
Ethernet Address
  - Unique worldwide (excepting errors)‏
  - Ethernet Only
Need to map from higher layer to lower
(i.e. IP to Ethernet, using ARP)‏

---
Address Resolution Protocol
ARP is only used in IPv4
  - ND replaces ARP in IPv6
- Check ARP cache for matching IP address
- If not found, broadcast packet with IP address to every host on Ethernet
- “Owner” of the IP address responds
- Response cached in ARP table for future use
- Old cache entries removed by timeout

---
ARP Procedure
1. ARP Cache is checked
5. ARP Entry is added
2. ARP Request is Sent using broadcast
4. ARP Reply is sent unicast
3. ARP Entry is added

---
ARP Table
43
07-01-20-08-73-22
192.168.0.34
120
05-02-20-08-88-33
192.168.0.65
3
08-00-20-08-70-54
192.168.0.2
Age (Sec)‏
Hardware Address
IP Address

---
Types of ARP Messages
ARP request
  - Who is IP addr X.X.X.X tell IP addr Y.Y.Y.Y
ARP reply
  - IP addr X.X.X.X is Ethernet Address hh:hh:hh:hh:hh:hh