Introduction to ISIS
Introduction to ISIS
AfNOG 2011 SI-E Workshop

---
IS-IS Standards History
IS-IS Standards History
ISO 10589 specifies OSI IS-IS routing protocol for CLNS traffic
  - A Link State protocol with a 2 level hierarchical architecture
  - Type/Length/Value (TLV) options to enhance the protocol
RFC 1195 added IP support
  - Integrated IS-IS
  - I/IS-IS runs on top of the Data Link Layer
  - Requires CLNP to be configured
- RFC5308 adds IPv6 address family support to IS-IS
- RFC5120 defines Multi-Topology concept for IS-IS
  - Permits IPv4 and IPv6 topologies which are not identical
  - (Required for an incremental roll-out of IPv6 on existing IPv4 infrastructure)

---
ISIS Levels
ISIS Levels
ISIS has a 2 layer hierarchy
  - Level-2 (the backbone)
  - Level-1 (the areas)
A router can be
  - Level-1 (L1) router
  - Level-2 (L2) router
  - Level-1-2 (L1L2) router

---
ISIS Levels
Level-1 router
  - Has neighbours only on the same area
  - Has a level-1 LSDB with all routing information for the area
Level-2 router
  - May have neighbours in the same or other areas
  - Has a Level-2 LSDB with all routing information about inter-area
Level-1-2 router
  - May have neighbours on any area.
  - Has two separate LSDBs: level-1 LSDB & level-2 LSDB

---
Backbone & Areas
Backbone & Areas
- ISIS does not have a backbone area as such (like OSPF)
- Instead the backbone is the contiguous collection of Level-2 capable routers
- ISIS area borders are on links, not routers
- Each router is identified with a unique Network Entity Title (NET)
  - NET is a Network Service Access Point (NSAP) where the n-selector is 0
  - (Compare with each router having a unique Router-ID with IP routing protocols)

---
L1, L2, and L1L2 Routers
L1, L2, and L1L2 Routers
Area-3
L1-only
L1L2
L2-only
Area-2
L1L2
L1L2
L1-only
Area-4
L1L2
L1-only
Area-1
L1L2
L1-only
[Speaker Notes: This slide just explains the concept of Areas and L1 vs L2 routers. It’s not a design recommendation!]

---
NSAP and Addressing
NSAP and Addressing
NSAP: Network Service Access Point
  - Total length between 8 and 20 bytes
  - Area Address: variable length field (up to 13 bytes)
  - System ID: defines an ES or IS in an area.
  - NSEL: N-selector. identifies a network service user (transport entity or the IS network entity itself)
NET: the address of the network entity itself

---
An Addressing Example
An Addressing Example
Area 3
49.0f01.0002.4444.4444.4444.00
49.0f01.0003.6666.6666.6666.00
Area 2
49.0f01.0002.3333.3333.3333.00
Area 4
49.0f01.0004.7777.7777.7777.00
49.0f01.0001.2222.2222.2222.00
49.0f01.0004.8888.8888.8888.00
Area 1
49.0f01.0001.1111.1111.1111.00

---
Addressing Common Practices
Addressing Common Practices
ISPs typically choose NSAP addresses thus:
  - First 8 bits – pick a number (usually 49)
  - Next 16 bits – area
  - Next 48 bits – router loopback address
  - Final 8 bits – zero
Example:
  - NSAP: 49.0001.1921.6800.1001.00
  - Router: 192.168.1.1 (loopback) in Area 1

---
Addressing & Design Practices
Addressing & Design Practices
ISPs usually only use one area
  - Multiple areas only come into consideration once the network is several hundred routers big
NET begins with 49
  - “Private” address range
All routers are in L2 only
  - Note that Cisco IOS default is L1L2
  - Set L2 under ISIS generic configuration (can also be done per interface)

---
Adjacencies
Adjacencies
- Hello Protocol Data Units (PDUs) are exchanged between routers to form adjacencies
- Area addresses are exchanged in IIH PDUs
  - Intermediate-System to Intermediate System Hello PDUs
  - (PDU is ISIS equivalent of a packet)
ISIS adjacency through IIH

---
Link State PDU (LSP)
Link State PDU (LSP)
- Each router creates an LSP and floods it to neighbours
- A level-1 router will create level-1 LSP(s)
- A level-2 router will create level-2 LSP(s)
- A level-1-2 router will create
  - level-1 LSP(s) and
  - level-2 LSP(s)

---
The ISIS LSP
The ISIS LSP
- LSPs have a Fixed Header and TLV coded contents
- The LSP header contains
  - LSP-id	Sequence number
  - Remaining Lifetime	Checksum
  - Type of LSP (level-1, level-2)
  - Attached bit	Overload bit
The LSP contents are coded as TLV (Type, Length, Value)
  - Area addresses
  - IS neighbours
  - Authentication Information

---
Link State Database Content
Link State Database Content
- Each router maintains a separate LSDB for level-1 and level-2 LSPs
- The LSDB contains:
  - LSP headers and contents
  - SRM bits: set per interface when router has to flood this LSP
  - SSN bits: set per interface when router has to send a PSNP for this LSP
[Speaker Notes: Partial Sequence Number PDU explained in next few slides]

---
Flooding of LSPs
Flooding of LSPs
- New LSPs are flooded to all neighbors
- All routers get all LSPs
- Each LSP has a sequence number
- There are 2 kinds of flooding:
  - Flooding on a p2p link
  - Flooding on LAN

---
Flooding on a p2p link
Flooding on a p2p link
- Once the adjacency is established both routers send CSNP packet
- Missing LSPs are sent by both routers if not present in the received CSNP
- Missing LSPs may be requested through PSNP
[Speaker Notes: CSNP - Complete Sequence Number PDU - explained in a few slides]

---
Flooding on a LAN
Flooding on a LAN
- Each LAN has a Designated Router (DIS)
- The DIS has two tasks
  - Conducting the flooding over the LAN
  - Creating and updating a special LSP describing the LAN topology (Pseudonode LSP)
DIS election is based on priority
  - Best practice is to select two routers and give them higher priority – then in case of failure one provides deterministic backup for the other
  - Tie break is by the highest MAC address

---
Flooding on a LAN
- DIS conducts the flooding over the LAN
- DIS multicasts CSNP every 10 seconds
- All routers on the LAN check the CSNP against their own LSDB (and may ask specific re-transmissions with PSNPs)

---
Complete Sequence Number PDU
Complete Sequence Number PDU
- Describes all LSPs in your LSDB (in range)
- If the LSDB is large, multiple CSNPs are sent
- Used on 2 occasions:
  - Periodic multicast by DIS (every 10 seconds) to synchronise the LSDB over LAN subnets
  - On p2p links when link comes up

---
Partial Sequence Number PDUs
Partial Sequence Number PDUs
- PSNPs Exchanged on p2p links (ACKs)
- Two functions
  - Acknowledge receipt of an LSP
  - Request transmission of latest LSP
PSNPs describe LSPs by its header
  - LSP identifier
  - Sequence number
  - Remaining lifetime
  - LSP checksum

---
Network Design Issues
Network Design Issues
- As in all IP network designs, the key issue is the addressing lay-out
- ISIS supports a large number of routers in a single area
- When network is so large requiring the use of areas, use summary-addresses
- >400 routers in the backbone is quite doable

---
Network Design Issues
Link cost
  - Default on all interfaces is 10
  - (Compare with OSPF which sets cost according to link bandwidth)
  - Manually configured according to routing strategy
Summary address cost
  - Equal to the best more specific cost
  - Plus cost to reach neighbor of best specific
Backbone has to be contiguous
  - Ensure continuity by redundancy
Area partitioning
  - Design so that backbone can NOT be partitioned

---
Scaling Issues
Scaling Issues
Areas vs. single area
  - Use areas where
    - sub-optimal routing is not an issue
    - areas with one single exit point
Start with L2-only everywhere
  - Future implementation of level-1 areas will be easier
  - Backbone continuity is ensured from start

---
Typical ISP Design
Typical ISP Design
49.0001.1921.6800.1006.00
49.0001.1921.6800.1004.00
PoP 3
PoP 2
49.0001.1921.6800.1003.00
PoP 4
49.0001.1921.6800.1007.00
49.0001.1921.6800.1002.00
49.0001.1921.6800.1008.00
PoP 1
49.0001.1921.6800.1001.00
All routers are in L2 only and only one area is used

---
Introduction to ISIS
AfNOG 2011 AR-E Workshop