Dynamic Routing
Dynamic Routing
Overview

---
Desirable Characteristics of Dynamic Routing
Desirable Characteristics of Dynamic Routing
- Automatically detect and adapt to topology changes
- Provide optimal routing
- Scalability
- Robustness
- Simplicity
- Rapid convergence
- Some control of routing choices
  - e.g., which links we prefer to use

---
Routers Talk Routing Protocols
Routers Talk Routing Protocols
Routing Protocol
IGP / EGP
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

---
Interplay between routing & forwarding
Interplay between routing & forwarding
Routing Protocol
IGP / EGP
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
value in arriving
packet’s header
1
0111
2
3

---
IP Routing – finding the path
IP Routing – finding the path
- Path is derived from information received from the routing protocol
- Several alternative paths may exist
  - best next hop stored in forwarding table
- Decisions are updated periodically or as topology changes (event driven)
- Decisions are based on:
  - topology, policies and metrics (hop count, filtering, delay, bandwidth, etc.)

---
IP Forwarding
IP Forwarding
- Router makes decision on which interface a packet is sent to
- Forwarding table populated by routing process
- Forwarding decisions:
  - Destination address
  - Class of service (fair queuing, precedence, others)
  - Local requirements (packet filtering)

---
Convergence – why do I care?
Convergence – why do I care?
- Convergence is when all the routers have a stable view of the network
- When a network is not converged there is network downtime
  - Packets don’t get to where they are supposed to go
    - Black holes (packets “disappear”)
    - Routing Loops (packets go back and forth between the same devices)
  - Occurs when there is a change in state of router or the links

---
Internet Routing Hierarchy
Internet Routing Hierarchy
- The Internet is composed of Autonomous Systems
- Each Autonomous System is an administrative entity that
  - Uses Interior Gateway Protocols (IGPs) to determine routing within the Autonomous System
  - Uses Exterior Gateway Protocols (EGPs) to interact with other Autonomous Systems

---
IGPs and EGPs
- IGPs provide routing information within your network (LAN, backbone links,etc)
- EGPs consider other networks outside your AS as a black box.

---
Internet Routing Architecture
Internet Routing Architecture
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous System: A collection of IP subnets and routers
under the same administrative authority.
Interior Routing Protocol
Exterior Routing Protocol

---
Interior Gateway Protocols
Interior Gateway Protocols
Four well known IGPs today
  - RIP
  - EIGRP
  - OSPF
  - ISIS

---
Exterior Gateway Protocols
Exterior Gateway Protocols
One single de-facto standard:
  - BGP

---
Routing’s 3 Aspects
Routing’s 3 Aspects
Acquisition of information about the IP subnets that are reachable through an internet
  - static routing configuration information
  - dynamic routing information protocols (e.g., BGP4, OSPF, RIP, ISIS)
  - each mechanism/protocol constructs a Routing Information Base (RIB)

---
Routing Aspect #2
Routing Aspect #2
Construction of a Forwarding Table
  - synthesis of a single table from all the Routing Information Bases (RIBs)
  - information about a destination subnet may be acquired multiple ways
  - a precedence is defined among the RIBs to arbitrate conflicts on the same subnet
  - Also called a Forwarding Information Base (FIB)

---
Routing #3
Routing #3
Use of a Forwarding Table to forward individual packets
  - selection of the next-hop router and interface
  - hop-by-hop, each router makes an independent decision

---
Routing versus Forwarding
Routing versus Forwarding
- Routing = building maps and giving directions
- Forwarding = moving packets between interfaces according to the “directions”
[Speaker Notes: 3]

---
IP Forwarding
Source
S
IP Subnet
IP Subnet
IP Subnet
Destination
IP Subnet
D
Forwarding decisions:
  - Destination address
  - class of service (fair queuing, precedence, others)
  - local requirements (packet filtering)

---
Routing Tables Feed the  Forwarding Table
Routing Tables Feed the Forwarding Table
BGP 4 Routing Table
ISIS – Link State Database
Static Routes
RIB
(ISIS)
Forwarding Information Base (FIB)
RIB
(BGP)
RIB
(Static)

---
RIB Construction
RIB Construction
- Each routing protocol builds its own Routing Information Base (RIB)
- Each protocol handles route “costs” in its own way.

---
FIB Construction
FIB Construction
- There is only ONE forwarding table!
- An algorithm is used to choose one next-hop toward each IP destination known by any routing protocol
  - the set of IP destinations present in any RIB are collected
  - if a particular IP destination is present in only one RIB, that RIB determines the next hop forwarding path for that destination
[Speaker Notes: Load balancing, if it is done, is a modification of the FIB creation. Multiple routes (usually with the same metric and usually only when there are multiple direct links to the same next-hop) are entered into the FIB and used to balance the load across the multiple links. The balancing can be done using round-robin, but a technique based on assigning hash codes to links in a round-robin fashion is typical. The has code is based on the source-destination address pair. This technique tends to keep datagrams that belong to the same communication in the order sent, thus reducing the amount of processing at the receiver.]

---
FIB Construction
Choosing FIB entries, cont..
  - if a particular IP destination is present in multiple RIBs, then a precedence is defined to select which RIB entry determines the next hop forwarding path for that destination
  - This process normally chooses exactly one next-hop toward a given destination
There are no standards for this; it is an implementation (vendor) decision

---
FIB Contents
FIB Contents
IP subnet and mask (or length) of destinations
  - can be the “default” IP subnet
- IP address of the “next hop” toward that IP subnet
- Interface id of the subnet associated with the next hop
- Optional: cost metric associated with this entry in the forwarding table

---
IP routing
IP routing
Default route
  - where to send packets if there is no entry for the destination in the routing table
  - most machines have a single default route
  - often referred to as a default gateway
  - 0.0.0.0/0
    - matches all possible destinations, but is usually not the longest match

---
IP route lookup: Longest match routing
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.00.00.00
vs.
10.0.0.0 & FF.00.00.00
Match! (length 8)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.FF.00.00
vs.
10.1.0.0 & FF.FF.00.00
Match! (length 16)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.00.00.00
vs.
20.0.0.0 & FF.00.00.00
No Match!

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & 00.00.00.00
vs.
0.0.0.0 & 00.00.00.00
Match! (length 0)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
This is the longest matching prefix (length 16). “R2” will send the packet to “R4”.

---
IP route lookup:
Longest match routing
Most specific/longest match always wins!!
  - Many people forget this, even experienced ISP engineers
Default route is 0.0.0.0/0
  - Can handle it using the normal longest match algorithm
  - Matches everything. Always the shortest match.

---
Distance Vector and Link State
Distance Vector and Link State
Distance Vector
  - Accumulates a metric hop-by-hop as the protocol messages traverse the subnets
Link State
  - Builds a network topology database
  - Computes best path routes from current node to all destinations based on the topology

---
Distance Vector Protocols
Distance Vector Protocols
- Each router only advertises to its neighbors, its “distance” to various IP subnets
- Each router computes its next-hop routing table based on least cost determined from information received from its neighbors and the cost to those neighbors

---
Why not use RIP?
Why not use RIP?
RIP is a Distance Vector Algorithm
  - Listen to neighbouring routes
  - Install all routes in routing table
    - Lowest hop count wins
  - Advertise all routes in table
    - Very simple, very stupid
- Only metric is hop count
- Network is max 16 hops (not large enough)
- Slow convergence (routing loops)
- Poor robustness

---
EIGRP
EIGRP
- “Enhanced Interior Gateway Routing Protocol”
- Predecessor was IGRP which was classfull
  - IGRP developed by Cisco in mid 1980s to overcome scalability problems with RIP
- Cisco proprietary routing protocol
- Distance Vector Routing Protocol
  - Has very good metric control
Still maybe used in some enterprise networks?
  - Multi-protocol (supports more than IP)
  - Exhibits good scalability and rapid convergence
  - Supports unequal cost load balancing

---
Link State Protocols
Link State Protocols

---
Link State Protocols
- Each router “multicasts” to all the routers in the network the state of its locally attached links and IP subnets
- Each router constructs a complete topology view of the entire network based on these link state updates and computes its next-hop routing table based on this topology view

---
Link State Protocols
- Attempts to minimize convergence times and eliminate non-transient packet looping at the expense of higher messaging overhead, memory, and processing requirements
- Allows multiple metrics/costs to be used

---
IS-IS
IS-IS
- “Intermediate System to Intermediate System”
- Selected in 1987 by ANSI as OSI intradomain routing protocol (CLNP – connectionless network protocol)
  - Based on work by DEC for DECnet/OSI (DECnet Phase V)
Extensions for IP developed in 1988
  - NSFnet deployed its IGP based on early ISIS-IP draft

---
IS-IS (cont)
IS-IS (cont)
Adopted as ISO proposed standard in 1989
  - Integrated ISIS supports IP and CLNP
Debate between benefits of ISIS and OSPF
  - Several ISPs chose ISIS over OSPF for a number of reasons.
- 1994-date: deployed by several larger ISPs
- Developments continuing in IETF in parallel with OSPF

---
OSPF
OSPF
Open Shortest Path First
  - “Open” means it is public domain
  - Uses “Shortest Path First” algorithm – sometimes called “the Dijkstra algorithm”
- IETF Working Group formed in 1988 to design an IGP for IP
- OSPF v1 published in 1989 – RFC1131
- OSPF v2 published in 1991 – RFC1247
- Developments continued through the 90s and today
  - OSPFv3 based on OSPFv2 designed to support IPv6

---
Link State Algorithm
Link State Algorithm
Each router contains a database containing a map of the whole topology
  - Links
  - Their state (including cost)
- All routers have the same information
- All routers calculate the best path to every destination
- Any link state changes are flooded across the network
  - “Global spread of local knowledge”

---
Summary
Summary
Now know:
  - Difference between static routes, RIP, OSPF and IS-IS.
  - Difference between Routing and Forwarding
  - A Dynamic Routing Protocol should be used in any ISP network
  - Static routes don’t scale
  - RIP doesn’t scale (and is obsolete)