Comparing ISIS and OSPF
Comparing ISIS and OSPF
AfNOG 2013

---
Comparing ISIS and OSPF
- Both are Link State Routing Protocols using the Dijkstra SPF Algorithm
- So what’s the difference then?
- And why do ISP engineers end up arguing so much about which is superior?

---
What Is IS-IS ?
What Is IS-IS ?
- Intermediate System to Intermediate System
- An “IS” is ISO terminology for a router
- IS-IS was originally designed for use as a dynamic routing protocol for ISO CLNP, defined in the ISO 10589 standard
- Later adapted to carry IP prefixes in addition to CLNP (known as Integrated or Dual IS-IS) as described in RFC 1195
- Predominantly used in ISP environment

---
IS-IS Timeline
IS-IS Timeline
1978ish “New” Arpanet Algorithm
  - Eric Rosen et al
1986 to 90 Decnet Phase V
  - Radia Perlman, Mike Shand
1987 ISO 10589 (IS-IS)
  - Dave Oran
1990 RFC 1195 (Integrated IS-IS)
  - Ross Callon, Chris Gunner
1990 to present: All sorts of enhancements
  - Everyone contributed!
2008 RFC5308 adds IPv6 support
  - And RFC5120 adds Multi-Topology Routing support

---
What Is OSPF ?
What Is OSPF ?
- Open Shortest Path First
- Link State Protocol using the Shortest Path First algorithm (Dijkstra) to calculate loop-free routes
- Used purely within the TCP/IP environment
- Designed to respond quickly to topology changes but using minimal protocol traffic
- Used in both Enterprise and ISP Environment

---
OSPF Timeline
OSPF Timeline
- Development began in 1987 by IETF
- OSPFv1 published in 1989 with RFC 1131
- OSPFv2 published in 1991 with RFC 1247
- Further enhancements to OSPFv2 in 1994 with RFC 1583 and in 1997 with RFC 2178
- Last revision was in 1998 with RFC 2328 to fix minor problems
- All above OSPF RFCs authored by John Moy
- RFC2740 introduced OSPFv3 (for IPv6) in 1999, replaced by RFC5340 in 2008
[Speaker Notes: OSPF on the Web: http://www.ietf.org/html.charters/ospf-charter.html Goals and Milestones: Jun 96 Complete OSPF for IPv6 specification and submit to IESG for consideration as a Proposed Standard. Jun 96 Document current usage, update OSPFv2 and submit to IESG for consideration as a Standard. Dec 96 Develop OSPF for IPv6 MIB and submit to IESG for consideration as a Proposed Standard. Dec 96 Submit Internet-Draft on ISPF extensions of IPv6 to IESG for consideration as a Proposed Standard. Jun 97 Update OSPF for IPv6 based on implementation experience, and submit to IESG for consideration as a Draft Standard. Done Gather operational experience with the OSPF protocol and submit the document as an Informational RFC. Done Develop multiple implementations, and test against each other. Done Obtain performance data for the protocol. Done Design the routing protocol, and write its specification. Done Make changes to the specification (if necessary) and publish the protocol as a Draft Standard RFC. Jun 98 Submit OSPF for IPv6 to IESG for consideration as a Standard.]

---
IS-IS & OSPF:   Similarities
IS-IS & OSPF:
Similarities
Both are Interior Gateway Protocols (IGP)
  - They distribute routing information between routers belonging to a single Autonomous System (AS)
With support for:
  - Classless Inter-Domain Routing (CIDR)
  - Variable Subnet Length Masking (VLSM)
  - Authentication
  - Multi-path
  - IP unnumbered links

---
IS-IS and OSPF Terminology
IS-IS and OSPF Terminology
OSPF
- Host
- Router
- Link
- Packet
- Designated router (DR)
- Backup DR (BDR)
- Link-State Advertisement (LSA)
- Hello packet
- Database Description (DBD)
ISIS
- End System (ES)
- Intermediate System (IS)
- Circuit
- Protocol Data Unit (PDU)
- Designated IS (DIS)
- N/A (no BDIS is used)
- Link-State PDU (LSP)
- IIH PDU
- Complete sequence number PDU (CSNP)

---
IS-IS and OSPF Terminology (Cont.)
IS-IS and OSPF Terminology (Cont.)
OSPF
- Area
- Non-backbone area
- Backbone area
- Area Border Router (ABR)
- Autonomous System Boundary Router (ASBR)
ISIS
- Sub domain (area)
- Level-1 area
- Level-2 Sub domain (backbone)
- L1L2 router
- Any IS

---
Transport
Transport
- OSPF uses IP Protocol 89 as transport
- IS-IS is directly encapsulated in Layer 2
Data Link Header
IP Header
OSPF Header
OSPF Data
Data Link Header
IS-IS Header
IS-IS Data

---
For Service Providers
For Service Providers
Which IGP should an ISP choose?
  - Both OSPF and ISIS use Dijkstra SPF algorithm
  - Exhibit same convergence properties
  - ISIS less widely implemented on router platforms
  - ISIS runs on data link layer, OSPF runs on IP layer

---
For Service Providers
Biggest ISPs tend to use ISIS – why?
  - In early 90s, Cisco implementation of ISIS was much more solid than OSPF implementation – ISPs naturally preferred ISIS
  - Main ISIS implementations more tuneable than equivalent OSPF implementations – because biggest ISPs using ISIS put more pressure on Cisco to implement “knobs”

---
For Service Providers
Moving forward a decade
  - Early Cisco OSPF implementation substantially rewritten
    - Now competitive with ISIS in features and performance
  - Router vendors wishing a slice of the core market need an ISIS implementation as solid and as flexible as that from Cisco
    - Those with ISIS & OSPF support tend to ensure they exhibit performance and feature parity

---
How to choose an IGP?
How to choose an IGP?
OSPF
  - Rigid area design – all networks must have area 0 core, with sub-areas distributed around
  - Suits ISPs with central high speed core network linking regional PoPs
  - Teaches good routing protocol design practices

---
How to choose an IGP?
ISIS
  - Relaxed two level design – L2 routers must be linked through the backbone
  - Suits ISPs with “stringy” networks, diverse infrastructure, etc, not fitting central core model of OSPF
  - More flexible than OSPF, but easier to make mistakes too

---
Other considerations
Other considerations
ISIS runs on link layer
  - Not possible to “attack” the IGP using IP as with OSPF
- ISIS’s NSAP addressing scheme avoids dependencies on IP as with OSPF
- Because biggest ISPs use ISIS, major router vendors tend to apply new optimisation features before they are added to OSPF

---
Comparing ISIS and OSPF
AfNOG 2013