Dynamic Routing
Overview

---
Desirable Characteristics of Dynamic Routing
Automatically detect and adapt to topology changes
Provide optimal routing
Scalability
Robustness
Simplicity
Rapid convergence
Some control of routing choices
e.g., which links we prefer to use

---
Routers Talk Routing Protocols
Routing Protocol
IGP / EGP
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

---
Interplay between routing & forwarding
Routing Protocol
IGP / EGP
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
value in arriving
packet’s header
1
0111
2
3

---
IP Routing – finding the path
Path is derived from information received from the routing protocol
Several alternative paths may exist
best next hop stored in forwarding table
Decisions are updated periodically or as topology changes (event driven)
Decisions are based on:
topology, policies and metrics (hop count, filtering, delay, bandwidth, etc.)

---
IP Forwarding
Router makes decision on which interface a packet is sent to
Forwarding table populated by routing process
Forwarding decisions:
Destination address
Class of service (fair queuing, precedence, others)
Local requirements (packet filtering)

---
Convergence – why do I care?
Convergence is when all the routers have a stable view of the network
When a network is not converged there is network downtime
Packets don’t get to where they are supposed to go
Black holes (packets “disappear”)
Routing Loops (packets go back and forth between the same devices)
Occurs when there is a change in state of router or the links

---
Internet Routing Hierarchy
The Internet is composed of Autonomous Systems
Each Autonomous System is an administrative entity that
Uses Interior Gateway Protocols (IGPs) to determine routing within the Autonomous System
Uses Exterior Gateway Protocols (EGPs) to interact with other Autonomous Systems

---
IGPs and EGPs
IGPs provide routing information within your network (LAN, backbone links, etc)
EGPs consider other networks outside your AS as a black box.

---
Internet Routing Architecture
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous
System (AS)
Autonomous System: A collection of IP subnets and routers
under the same administrative authority.
Interior Routing Protocol
Exterior Routing Protocol

---
Interior Gateway Protocols
Four well known IGPs today
RIP
EIGRP
OSPF
ISIS

---
Exterior Gateway Protocols
One single de-facto standard:
BGP

---
Routing’s 3 Aspects: #1
Acquisition of information about the IP subnets that are reachable through an internet
static routing configuration information
dynamic routing information protocols (e.g., BGP4, OSPF, RIP, ISIS)
each mechanism/protocol constructs a Routing Information Base (RIB)
“Building a map”

---
Routing Aspect #2
Construction of a Forwarding Table
synthesis of a single table from all the Routing Information Bases (RIBs)
information about a destination subnet may be acquired multiple ways
a precedence is defined among the RIBs to arbitrate conflicts on the same subnet
Also called a Forwarding Information Base (FIB)
“Using the map to plan a journey”
Actually, to plan journeys to all known destinations

---
Routing #3
Use of a Forwarding Table to forward individual packets
selection of the next-hop router and interface
hop-by-hop, each router makes an independent decision
“Using the journey plan to choose a direction at each intersection”

---
Routing versus Forwarding
Routing = building maps and giving directions
Forwarding = moving packets between interfaces according to the “directions”
[Speaker Notes: 3]

---
IP Forwarding
Source
S
IP Subnet
IP Subnet
IP Subnet
Destination
IP Subnet
D
Forwarding decisions:
Destination address
class of service (fair queuing, precedence, others)
local requirements (packet filtering)

---
Routing Tables Feed the Forwarding Table
BGP 4 Routing Table
ISIS – Link State Database
Static Routes
RIB
(ISIS)
Forwarding Information Base (FIB)
RIB
(BGP)
RIB
(Static)

---
RIB Construction
Each routing protocol builds its own Routing Information Base (RIB)
Each protocol handles route “costs” in its own way.

---
FIB Construction
There is only ONE forwarding table!
An algorithm is used to choose one next-hop toward each IP destination known by any routing protocol
the set of IP destinations present in any RIB are collected
if a particular IP destination is present in only one RIB, that RIB determines the next hop forwarding path for that destination
[Speaker Notes: Load balancing, if it is done, is a modification of the FIB creation. Multiple routes (usually with the same metric and usually only when there are multiple direct links to the same next-hop) are entered into the FIB and used to balance the load across the multiple links. The balancing can be done using round-robin, but a technique based on assigning hash codes to links in a round-robin fashion is typical. The has code is based on the source-destination address pair. This technique tends to keep datagrams that belong to the same communication in the order sent, thus reducing the amount of processing at the receiver.]

---
FIB Construction
Choosing FIB entries, cont..
if a particular IP destination is present in multiple RIBs, then a precedence is defined to select which RIB entry determines the next hop forwarding path for that destination
This process normally chooses exactly one next-hop toward a given destination
There are no standards for this; it is an implementation (vendor) decision

---
FIB Contents
IP subnet and mask (or length) of destinations
can be the “default” IP subnet
IP address of the “next hop” toward that IP subnet
Interface id of the subnet associated with the next hop
Optional: cost metric associated with this entry in the forwarding table

---
IP routing
Default route
where to send packets if there is no entry for the destination in the routing table
most machines have a single default route
often referred to as a default gateway
0.0.0.0/0
matches all possible destinations, but is usually not the longest match

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.00.00.00
vs.
10.0.0.0 & FF.00.00.00
Match! (length 8)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.FF.00.00
vs.
10.1.0.0 & FF.FF.00.00
Match! (length 16)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & FF.00.00.00
vs.
20.0.0.0 & FF.00.00.00
No Match!

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
10.1.1.1 & 00.00.00.00
vs.
0.0.0.0 & 00.00.00.00
Match! (length 0)

---
IP route lookup:
Longest match routing
R3
Most of 10.0.0.0/8 except for
10.1.0.0/16
Packet: Destination
IP address: 10.1.1.1
R4
R2
R1
10.1.0.0/16
Based on destination IP address
R2’s IP forwarding table
10.0.0.0/8  R3
10.1.0.0/16  R4
20.0.0.0/8  R5
0.0.0.0/0  R1
This is the longest matching prefix (length 16). “R2” will send the packet to “R4”.

---
IP route lookup:
Longest match routing
Most specific/longest match always wins!!
Many people forget this, even experienced ISP engineers
Default route is 0.0.0.0/0
Can handle it using the normal longest match algorithm
Matches everything. Always the shortest match.
IPv6 equivalent is 0:0:0:0:0:0:0:0/0 or just “::/0”

---
Distance Vector and Link State
Distance Vector
Accumulates a metric hop-by-hop as the protocol messages traverse the subnets
Link State
Builds a network topology database
Computes best path routes from current node to all destinations based on the topology

---
Distance Vector Protocols
Each router only advertises to its neighbors, its “distance” to various IP subnets
Each router computes its next-hop routing table based on least cost determined from information received from its neighbors and the cost to those neighbors

---
Why not use RIP?
RIP is a Distance Vector Algorithm
Listen to neighbouring routes
Install all routes in routing table
Lowest hop count wins
Advertise all routes in table
Very simple, very stupid
Only metric is hop count
Network is max 16 hops (not large enough)
Slow convergence (routing loops)
Poor robustness

---
EIGRP
“Enhanced Interior Gateway Routing Protocol”
Predecessor was IGRP which was classfull
IGRP developed by Cisco in mid 1980s to overcome scalability problems with RIP
Cisco proprietary routing protocol
Distance Vector Routing Protocol
Has very good metric control
Still maybe used in some enterprise networks?
Multi-protocol (supports more than IP)
Exhibits good scalability and rapid convergence
Supports unequal cost load balancing

---
Link State Protocols

---
Link State Protocols
Each router “multicasts” to all the routers in the network the state of its locally attached links and IP subnets
Each router constructs a complete topology view of the entire network based on these link state updates and computes its next-hop routing table based on this topology view

---
Link State Protocols
Attempts to minimize convergence times and eliminate non-transient packet looping at the expense of higher messaging overhead, memory, and processing requirements
Allows multiple metrics/costs to be used

---
IS-IS
“Intermediate System to Intermediate System”
Selected in 1987 by ANSI as OSI intradomain routing protocol (CLNP – connectionless network protocol)
Based on work by DEC for DECnet/OSI (DECnet Phase V)
Extensions for IP developed in 1988
NSFnet deployed its IGP based on early ISIS-IP draft

---
IS-IS (cont)
Adopted as ISO proposed standard in 1989
Integrated ISIS supports IP and CLNP
Debate between benefits of ISIS and OSPF
Several ISPs chose ISIS over OSPF for a number of reasons.
1994-date: deployed by several larger ISPs
Developments continuing in IETF in parallel with OSPF

---
OSPF
Open Shortest Path First
“Open” means it is public domain
Uses “Shortest Path First” algorithm – sometimes called “the Dijkstra algorithm”
IETF Working Group formed in 1988 to design an IGP for IP
OSPF v1 published in 1989 – RFC1131
OSPF v2 published in 1991 – RFC1247
Developments continued through the 90s and today
OSPFv3 based on OSPFv2 designed to support IPv6

---
Link State Algorithm
Each router contains a database containing a map of the whole topology
Links
Their state (including cost)
All routers have the same information
All routers calculate the best path to every destination
Any link state changes are flooded across the network
“Global spread of local knowledge”

---
Summary
Now know:
Difference between static routes, RIP, OSPF and IS-IS.
Difference between Routing and Forwarding
A Dynamic Routing Protocol should be used in any ISP network
Static routes don’t scale
RIP doesn’t scale (and is obsolete)